## Slide 1
Accelerometer Sensor Data (Case Western Reserve University)
  12,000 samples per second
  Inner raceway bearing sensor – drive end
  Data segmented into fixed sizes of 256 samples
  14,234 segments total
  6,633 Baseline (normal) segments
  7,601 Faulty segments
Classification Problem
  4 Baseline (normal) classes
  16 Faulty classes
  20 Total classes
Contemporary Approach : 1D CNN
Classic Approach : Engineered Features
  Fast Fourier Transform
  Discrete Wavelet Transform
  Fast Fourier Transform + Discrete Wavelet Transform
  SVM, XGBoost, Gradient Boosting, Random Forests
Summary of Project

## Slide 2
Summary of Project – Data Class Descriptions
Label | Segments | Data Type | Data Description | File Name
0 | 952 | Baseline Data | 0 HP workload normal | 97.mat
1 | 1890 | Baseline Data | 1 HP workload normal | 98.mat
2 | 1894 | Baseline Data | 2 HP workload normal | 99.mat
3 | 1897 | Baseline Data | 3 HP workload normal | 100.mat
4 | 473 | Faulty Data | 0 HP workload .007 inches EDM | 105.mat
5 | 475 | Faulty Data | 0 HP workload .014 inches EDM | 169.mat
6 | 477 | Faulty Data | 0 HP workload .021 inches EDM | 209.mat
7 | 471 | Faulty Data | 0 HP workload .028 inches EDM | 3001.mat
8 | 476 | Faulty Data | 1 HP workload .007 inches EDM | 106.mat
9 | 475 | Faulty Data | 1 HP workload .014 inches EDM | 170.mat
10 | 474 | Faulty Data | 1 HP workload .021 inches EDM | 210.mat
11 | 474 | Faulty Data | 1 HP workload .028 inches EDM | 3002.mat
12 | 477 | Faulty Data | 2 HP workload .007 inches EDM | 107.mat
13 | 475 | Faulty Data | 2 HP workload .014 inches EDM | 171.mat
14 | 475 | Faulty Data | 2 HP workload .021 inches EDM | 211.mat
15 | 474 | Faulty Data | 2 HP workload .028 inches EDM | 3003.mat
16 | 480 | Faulty Data | 3 HP workload .007 inches EDM | 108.mat
17 | 475 | Faulty Data | 3 HP workload .014 inches EDM | 172.mat
18 | 476 | Faulty Data | 3 HP workload .021 inches EDM | 212.mat
19 | 474 | Faulty Data | 3 HP workload .028 inches EDM | 3004.mat
EDM - electro-discharge machining was used to create faulty bearings

## Slide 3
Engineered Features using FFT
Raw Signal
FFT
Autocorrelation
Plot
Feature Extraction
Amplitude
Plot
PSD
Plot
Classification
ML
Algorithms
PSD – Power Spectral Density
Feature Extraction selects top n peaks of each plot

## Slide 4
Engineered Features using DWT
Coefficients for High Frequencies
at each Level
Final Low Frequency
Coefficients
Feature Extraction
Classification
ML
Algorithms
Feature Extraction
Entropy
Statistics
Crossings

## Slide 5
CNN 1D Architecture
s1
s2
.
.
.
s16
s17
s18
.
.
.
s32
.
.
.
s256
Kernel Size = 16
Strides = 1
Window steps through data (256 times with padding)
Feature Map
64 Filtered Feature Maps
.
.
.
Convolution
. . .
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
. . .
.
.
.
64 Feature Maps
Pooled Results
Pool Size = 8
Reduces size from 256 to 256/8 = 32
Constructs a value by taking max of 8 values
Pooling
Filtering
8 values
ReLu Applied

## Slide 6
CNN 1D Architecture

## Slide 7
CNN 1D Architecture – Sensor Data
Convolution
Convolution
ReLu
ReLu
Pooling
Pooling
Flatten
1-D Convolution Neural Network Model
Input
Results
Filters = 64
Kernel Size = 16
Pool Size = 8
Batch Size = 16
Activation = Relu
Filters = 256
Kernel Size = 16
Pool Size = 8
Batch Size = 16
Activation = Relu
Classification

## Slide 8
. . . .
v1
v2
v3
v4
vn
Data Preparation: Training Set
Sensor Signal (12,000 samples/second)
Time
Size of vi is fixed at 256.
Where n is the number of fixed sample vectors of size 256
yi is the label for signal vector vi. yi in (0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,15,16,17,18,19)

## Slide 9
. . . .
vn+1
vn+2
vn+3
vn+4
vn+m
Size of vi is fixed at 256.
Where m is the number of fixed sample vectors of size 256
yi is the label for signal vector vi. yi in (0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,15,16,17,18,19)
Data Preparation: Test Set
Time
Sensor Signal (12,000 samples/second)

## Slide 10
. . . .
v1
v2
v3
v4
vn
. . .
v1
v2
v3
vn
Results
1-D Convolution Neural Network Model
Signal Data Input
Training Set
Contemporary Approach - Training
Training set is further subdivided into training and validation
Vi is fixed at 256 samples
Convolution
Convolution
ReLu
ReLu
Pooling
Pooling
Flatten
Classification

## Slide 11
. . . .
vn+1
vn+2
vn+3
vn+4
vn+m
. . .
vn+1
vn+2
vn+3
vn+m
Results
1-D Convolution Neural Network Model
Signal Data Input
Test Set
Convolutional Neural Network - Testing
Convolution
Convolution
ReLu
ReLu
Pooling
Pooling
Dense

## Slide 12
. . . .
v1
v2
v3
v4
vn
. . .
v1
v2
v3
vn
Signal Data Input
Training Set
Classic Approach- Training
Vi is fixed at 256 samples
Feature
Extraction
(FFT and DWT)
ML Classification Algorithms
(XGB, GB, RF, SVC, Knn)
Results
Feature Engineering and Classification

## Slide 13
CNN 1D Feature Extraction
Convolution
Convolution
ReLu
ReLu
Pooling
Pooling
1-D Convolution Neural Network Model
Input
Results
Filters = 64
Kernel Size = 16
Pool Size = 8
Batch Size = 16
Activation = Relu
Filters = 256
Kernel Size = 16
Pool Size = 8
Batch Size = 16
Activation = Relu
Feature Extraction
Flatten

## Slide 14
. . . .
v1
v2
v3
v4
vn
. . .
v1
v2
v3
vn
Signal Data Input
Training Set
Classic and Contemporary Approach Together
Vi is fixed at 256 samples
Feature
Extraction
(FFT, DWT & 1D CNN)
ML Classification using
XGBoost
Results
Feature Engineering and Classification

## Slide 15
Prediction and Results using Testing Data